## Slide 1: MAGNETOMETER-LESS STATE-ESTIMATION OF A MOBILE ROBOT USING CASCADED KALMAN FILTERS
By Tommy Le
Advisor: Dr. Ji-Chul Ryu 10/13/2023

## Slide 2: Outline
Introduction
Previous Work
Objective
Framework
  Preprocessing methods
  Mobile Robot Extended Kalman Filter
  IMU Extended Kalman Filter
Simulation Results
Remaining Work

## Slide 3: Background
Mobile robot localization
  Outdoor
    GPS
  Indoor
    Magnetometer, UWB
  Both
    Encoders, vision systems
[1] E. North, J. Georgy, M. Tarbouchi, U. Iqbal and A. Noureldin, “Enhanced Mobile Robot Outdoor Localization Using INS/GPS Integration,” IEEE Explore, Jan. 2010.
Common Outdoor Localization Framework [1]

## Slide 4: Background
Inertial Measurement Units (IMUs)
  Tri-axial accelerometer, gyroscope
    Sometimes magnetometer
  Used for pose information
Errors
  Accelerometer has high frequency noise
  Gyroscope suffers from drift
[2] “Pololu - AltIMU-10 v5 Gyro, Accelerometer, Compass, and Altimeter (LSM6DS33, LIS3MDL, and LPS25H Carrier),” www.pololu.com. https://www.pololu.com/product/2739 (accessed Oct. 09, 2023).
‌
Pololu 10 DOF IMU [2]

## Slide 5: Motivation
Desire small spherical robot for indoor navigation
  Experiments with common lab animals
Magnetometer suffered due to placement of motors
Other sensors do not fit size requirement

## Slide 6: Previous Work
Pose Estimation of a Mobile Robot Based on Fusion of IMU Data and Vision Data Using an Extended Kalman Filter [3]
  Object recognition and feature matching
  State transition matrices are IMU and vision
  4 wheeled mobile robot
[3] M. Alatise and G. Hancke, “Pose Estimation of a Mobile Robot Based on Fusion of IMU Data and Vision Data Using an Extended Kalman Filter,” Sensors, vol. 17, no. 10, p. 2164, Sep. 2017, doi: https://doi.org/10.3390/s17102164.
‌

## Slide 7: Previous Work
Localization and Trajectory Tracking of an Autonomous Spherical Rolling Robot Using IMU and Odometry [4]
  Encoders
    Requires wheel odometry
  Magnetometer
    Larger robot to isolate magnetic distortion
  Dead reckoning for localization
[4] V. Ajay, A. Suherlan, G. Soh, S. Foong, K. Wood and K. Otto, “Localization and trajectory Tracking of an Autonomous Spherical Rolling Robot using IMU and Odometry ,” ASME, Aug. 2015.‌

## Slide 8: Previous Work
Enhanced 3D Kinematic Modeling of Wheeled Mobile Robots [5]
  No real-time implementation
  Able to provide robust estimation with just a kinematic model
[5] A. Kelly and N. Seegmiller, “Recursive kinematic propagation for wheeled mobile robots,” The International Journal of Robotics Research, vol. 34, no. 3, pp. 288–313, Jan. 2015, doi: https://doi.org/10.1177/0278364914551773.

## Slide 9: Previous Work
Enhanced Pedestrian Navigation Based on Course Angle Error Estimation Using Cascaded Kalman Filters [6]
  IMU to estimate pedestrian pose
    INS-PDR-EKF
    Magnetometer course correction
  Cascaded KF framework
[6] J. Song and C. Park, “Enhanced Pedestrian Navigation Based on Course Angle Error Estimation Using Cascaded Kalman Filters,” Sensors, vol. 18, no. 4, p. 1281, Apr. 2018, doi: https://doi.org/10.3390/s18041281.

## Slide 10: Objectives
Develop a robust magnetometer-less state estimation algorithm using only IMU data
Design the algorithm so it can incorporate additional sensor data to improve estimation

## Slide 11: Kalman Filter Review
Kalman Filter
  Designed for linear systems
  Follows predict and update model
  Applications
    Pose estimation
    Economics
    Weather forecasting
[7] W. Franklin, “Kalman Filter Explained Simply,” The Kalman Filter, Dec. 31, 2020. https://thekalmanfilter.com/kalman-filter-explained-simply/
Kalman Filter Flow Chart [7]

## Slide 12: Kalman Filter Review
Extended Kalman Filter
  Extension for nonlinear systems
  Linearizes using Jacobians
[8] K. Kitani, “Extended Kalman Filter,” Computer Vision CMU. https://www.cs.cmu.edu/~16385/s17/Slides/16.4_Extended_Kalman_Filter.pdf/
Linearization using the Jacobian and Taylor Expansion [8]

## Slide 13: Kalman Filter Review
Cascaded Kalman Filter
  Alternative to augmenting states
  Small computation amount
  high data rate
  strong real-time performance
Pros | Cons
Simpler | Sequential Processing
Modular | Complexity tuning
Computationally cheaper | 
[9] Y. Li, C. Liang, M. Lu, X. Hu, and Y. Wang, “Cascaded Kalman filter for target tracking in automotive radar,” The Journal of Engineering, vol. 2019, no. 19, pp. 6264–6267, Oct. 2019, doi: https://doi.org/10.1049/joe.2019.0159.

## Slide 14: Overall Framework

## Slide 15: Preprocessing: NMNI
[10] M. L. Hoang, A. Pietrosanto, S. D. Iancono, and V. Paciello, “Pre-Processing Technique for Compass-less Madgwick in Heading Estimation for Industry 4.0,” ieeexplore.ieee.org, Jun. 30, 2020.
No Motion No Integration
  Filters gyroscope data
  Bias compensation
  Store and update threshold
  Check for motion
NMNI Flow chart [10]

## Slide 16: Preprocessing: NDZTA
[11] M. L. Hoang, M. Carratu, M. A. Ugwiri, V. Paciello, and A. Pietrosanto, “A New Technique for Optimization of Linear Displacement Measurement based on MEMS Accelerometer,” ieeexplore.ieee.org, Nov. 30, 2020.
No Displacement Zero Translational Accumulation
  Filters accelerometer data
  Low-pass Filter
  Store and update threshold
  Check for motion
NDZTA Flow Chart [11]

## Slide 17: Pre-processing: Complementary Filter
Sensor fusion algorithm for orientation estimation
[12] M. Shah, S. Bhargava, and S. B. K. Mr, “ Mission Planning and Waypoint Navigation of a Micro Quad Copter by Selectable GPS Co-Ordinates,” ResearchGate.
Complementary Filter Diagram [12]

## Slide 18: 1st Kalman Filter (Mobile Robot): Process Model
Unicycle Model Mobile Robot
States and Measurements
  X, Y, and heading
Unicycle Model Mobile Robot Diagram

## Slide 19: 1st Kalman Filter (Mobile Robot): Measurement Model
Measurements are transformed externally

## Slide 20: Overall Framework

## Slide 21: 2nd Kalman Filter (IMU): Process Model

## Slide 22: 2nd Kalman Filter (IMU): Measurement Model
Measurements
  Heading error
  Velocity

## Slide 23: Simulation Results
Ground Truth
  Generated from unicycle model kinematics
  Testing with circular motion
    Time: 0 - 4 sec with 20 ms refresh rate
Measurements generated from ground truth
  Drift modeled

## Slide 24: Simulation Results
Preprocessing methods only

## Slide 25: Simulation Results
  EKF without error compensation

## Slide 26: Simulation Results
  Fully compensated trajectory estimation

## Slide 27: Simulation Results
Estimated heading

## Slide 28: Simulation Results
Estimated velocity

## Slide 29: Remaining Work
Fusion of optional additional sensor
Development in ROS Gazebo
Physical Implementation
  Sphero-mini
  Overhead camera for ground truth

## Slide 30: Optional Sensor Block
Vision System
  Provides position data
  Minimize a cost function of squared errors
    Either position or interpolated heading
  Pass to 1st EKF (mobile robot)

## Slide 31: Gazebo Development
Develop algorithm without need for physical system
Easily transfer program to robot
[13] R. Telez, “Developing ROS programs for the Sphero robot,” The Construct, Mar. 09, 2017. https://www.theconstructsim.com/developing-for-sphero/ (accessed Oct. 09, 2023).
Sphero is Gazebo Environment for Maze Navigation [13]

## Slide 32: Physical implementation
Sphero-Mini
  40 mm Diameter
  6DOF IMU
  Dual wheel drive
[14] “Steam Education for All Ages & Stages.” STEM Kits & Robotics for Kids | Inspire STEM Education with Sphero, https://sphero.com/.
Sphero-Mini [14]
Vision system and workspace

## Slide 33: Physical Implementation
Vision-based control package created using ROS
[15] T. Le, “sphero_ros_interaction,” GitHub, May 04, 2023. https://github.com/TaiLe2435/sphero_ros_interaction (accessed Oct. 09, 2023).
Demonstration of Vision-Based Control Package with Sphero-Mini [15]

## Slide 34: Potential Challenges
Slip in Sphero-mini
Interpolated heading error
ROS operating speed

## Slide 35: Timeline